## Slide 1: CAPTAIN STEEL PVT LIMITED
Presenting the TMT Bar manufacturing Process
Notes: JOURNY TO “CAPTAIN TMT” MANUFACTURING PROCESS

## Slide 2: WELCOME TO CAPTAIN HOUSE

## Slide 3: PLANT AT KADUWELLA & MALWANNA
LET US START A JOURNY TO “CAPTAIN TMT”
MANUFACTURING PROCESS

## Slide 6: QCD
Testing of billet’s chemical composition by Spectrometer.

## Slide 7
C | 0.22%(Max)
S | 0.035%(Max)
P | 0.04%(Max)
Mn | 0.5%-0.7%
Si | < 0.20%
CE | 0.3%-0.45%
BILLETS
Chemical Analysis

## Slide 8: Journey towards Rolling Mills
Billets to oil fired furnace.
Hot billets to mills.
TMT through Quenching box.
Automatic cooling bed.
FG testing.
100 feet Chimney for Flue gas emission.
Full bearing mills for negligible sound.
PLC automation.
Treated water recycling.
Ambient cooling.

## Slide 9: RMD
Charging of billets to RMD re-heating furnace

## Slide 11: RMD
Oil fired furnace is preparing the 2.5 M (x 2) long 130mm billets in rolling condition by heating approx 1170ᴼ C at its Soaking Zone. The ready billets are being discharged by the help of Ejector.

## Slide 12: RMD
Red Hot billets are coming out of re-heating furnace

## Slide 16: RMD
Material passing one stand to other in continuous mills.

## Slide 19
COMPLETE TMT SYSTEM
Tmt system

## Slide 20: TMT THEORY
TMT TREATMENT GRAPH
ROLLED BAR TMT TREATMENT

## Slide 21: Phase Changes During The Process

## Slide 22
These quenched and tempered martensite rebars have a uniform hardened tempered martensite periphery(15-30 per cent of area)with softer ferrite pearlite core and are good for civil construction.
This is an “over quenched ” bar.The hardened periphery is about 60% of the cross section area.Such bars will have poor ductility and are bad for civil construction
This shows a non-uniform hardened periphery.Owing to incorrect mill operation or an improper quenching system, quenching did not occur all around.Such bars are only to be used after extensive testing.
This is a bar produced by a bad quenching system or”hit and trial”TMT technology.Properties will vary widely from bar to bar and such bars should never be used in civil construction.
TMT Bars

## Slide 23: Inspection at TMT Plant
Incoming material temperature
Water temperature
Water pressure
Outgoing material temperature
Linear speed of finished material
Equalising temperature at the cooling bed

## Slide 25
270
250
230
210
190
170
150
130
770
710
650
590
530
470
410
HARDNESS
HV
SURFACE
CORE
N/mm2
TENSILE STRENGTH
25 mm TMT BAR
HARDNESS VS TENSILE STRENGTH
FIG INDICATES THE HARDNESS (HV) VS TENSILE STRENGTH TMT BAR FROM THE SURFACE TO CORE

## Slide 26: RMD
TMT are being transferred towards a roller track after ambient cooling. Finally cold TMT are travelling towards Cold Shearing Machine for cutting in 6 M to 12 M length.

## Slide 27: RMD - QCD
UTM – Tensely testing is under process before bundling for dispatch.

## Slide 28: QCD - RMD
After proper testing (bend test), material are staging for despatch.

## Slide 30
Notes: High Ductility Test and Captain RB 500 results……………………………………………………..

## Slide 31
Notes: Ductility curve of CAPTAIN RB500 ……………………………………………………………….

## Slide 33: DISPATCH SECTION
Bundling as per required numbers of bars & section

## Slide 34: RMD – ELECTRICAL DEPT
Total operations are being controlled by pulpit operators, through PLC.

## Slide 35: RMD - ELECTRICAL
“NELCO” make control panels (with collaboration of an Italian company) are installed for total rolling mills operation.

## Slide 36: Most sophisticated Workshop for maintenance of RMD

## Slide 38: Impressions on the Rolls by CNC machine

## Slide 39
TMT-BAR with others
Comparison of
Elongation | Y/s, N/m2 | Remarks
18%-22% | 500-550 | TMT bar
36%-45% | 265-300 | Bars without Any treatment
32%- 40% Or below 6% | 360-390 Or 600 & above | Bars with inadequate/ Improper treatment

## Slide 40
The 7 C’s Of THE “CAPTAIN” PARIVAR
Common - Purpose, Goal
Control - Leader
Context - Why ?
Capabilities
Commitment
Collaboration
communication

## Slide 41
WHY CAPTAIN TMT IS BETTER ?
CAPTAIN TMT bars are produced with global Turbo Quench Technology from GERMANY. It conforms to all National and International standards. The Best combination of chemical & physical properties is the main characteristic of CAPTAIN TMT. Strict Quality Control is maintained at each level of production. CAPTAIN TMT bars are of uniform strength, elongation and enhanced ductility that is far in excess of minimum limits specified in the SLS standard . As per the SLS and practically used by designers bars require minimum yield strength of 500 N/mm2. However CAPTAIN TMT bars possess typical yield strength as high as 525 & 550 N/mm2. Further as per BS/SLS standard ductility as measured elongation is specified to be 14.5 % which is tested to be 18 % in case of CAPTAIN TMT. Hence the bars produced with international technology are much better than traditional cold twisted deformed (CTD) bars.

## Slide 42
Notes: “ LESSER GROUND OCCUPIED BUT HIGHER ACCOMMODATION OBTAINED DUE TO SKY SCRAPERS “

## Slide 48: THANK YOU
“We will request our dealer/distributor to make an arrangement for visit of our plant to establish the realistic pointer view of this presentation”

## Slide 54: “Wish you be safe in life with CAPTAIN TMT bars” Thank you.